## Slide 1: GEp5
Focal Plane Polarimeter
  Front tracker
  Back tracker GEM 128 K channels
  288 channels HCAL on FADC ( 10 samples )
Electron detector
  1800 channels ECAL
  CDet 2152 Channels ( TDC )

## Slide 2: GEM data flow GEp
GEM
153 640
strips
MPD
153 640
X 6 samples x 3 bytes
FT=5.99 GB/s
BT=10.2 GB/s
Total= 16.2 GB/s
5 KHz trigger rate
MPD
Zero suppress
FT=1.63GB/s
BT=2.76 GB/s
Geometrical cut (factor 3)
FT=0.53 GB/s
BT=0.9 GB/s
Analog
SSP
Deconvolution
( factor 2)
FT=0.26 GB/s
BT=0.45GB/s
Keep Amplitude and time (3)
FT=0.09 GB/s
BT=0.15 GB/s
Total
240 MB/s
Time window | 6x25 ns | 3x25 ns
Occupancy forward tracker in % | 36.2 | 18.1
Occupancy back tracker In % | 22.4 | 11.2
Need to test clustering and correlations betweens planes for further reduction
Assume 2.5 strips cluster size

## Slide 3: GEp5 event size ( after deconvolution and geomtrical matching)
Detector | Channels | Single rate Hz | Occupancy 75 ns in % | Channels firing | Event size (bytes) | Data rate 5 KHz MB/s
Front tracker | 41,000 | 3.3e9 | 18.1 | 7430 | 136,000 | 90
Back tracker | 128,000 | 3.36e9 | 22.4 | 12600 | 230,000 | 150
HCal | 288 | _ | 100 | 288 | 7,200 | 36
ECAL | 1800 + 225 | _ | 100 | 2025 | 8,100 | 45
CDET | 2152 | _ | 10 | 216 | 864 | 4.3
Total |  |  |  |  |  | 325.3 MB/s
HCAL and ECAL occupancies need to be evaluated : using 100 % for now

## Slide 4
ECAL
1800
Channels
225 sums
HCAL
288
Channels
Optical 83x100 Mbit=10 GB/s
GEM
153,640
Channels
Analog
MPD
83 Boards
16.2 GB/s in
1430 MB/s out
(zero suppress, matching)
SSP
3 Boards
1430 MB/s in
Deconvolution
715 MB/s
Keep A and T
240 MB/s
VME
CPU
VME bus 3x100 MB/s
DAQ
Computer
325.3 MB/s
CDet
1176x2=
2352
Channels
FADC
18
Boards
36 MB/s
VME
CPU
VME bus 2x100 MB\s
1 Gbit
Ethernet x3
= 375 MB/s max
1 Gbit Ethernet x2
= 250 MB/s max
Fastbus
96 Boards in 12 crates
45 MB/s = 3.5 MB/s per crate
Fastbus
87 boards in 9 crates
Boards
4.3 MB/s = 1.1 MB/s crate
Swi
tch
1 Gbit Ethernet
x12
100 Mbit Ethernet
x9
1 Gbit Ethernet x2
250 MB/s max
VME
CPU
VME bus 12x20 MB\s
VME
CPU
VME bus 9x20 MB\s
Typical SSD
has
500 MB/s rate

## Slide 5: GEn and GMn
Bigbite
  GEM 128 K channels
  Shower 189 blocks (ADC)
  Preshower 54 blocks (ADC)
  Scintillator 180 bars 360 PMTs ( ADC/TDC)
  Cerenkov 550 PMTs (TDC)
Neutron detector
  288 channels HCAL ( FADC + high res TDC )
  CDet 2152 Channels ( TDC )

## Slide 6: Gen trigger rates ( 95 % QE peak )
Q^2 | Rate [kHz]
1.5 | 3
4 | 0.4
7 | 0.09
10 | 0.06

## Slide 7: GEM data flow GEp
GEM
112 640
strips
55 MPDs
112 640
X 6 samples x 3 bytes
= 10.3 GB/s
5 KHz trigger rate
MPD
Zero suppress
= 1.8 GB/s
Analog
SSP
Deconvolution
( factor 2)
= 0.9 GB/s
Keep A & T
(factor 3)
=0.3 GB/s
Time window | 6x25 ns | 3x25 ns
Occupancy back tracker In % | 17.4 | 8.7
Assume each MPD word packed on 24 bits = 3 bytes

## Slide 8: Gen and GMn event size
Arm | Detector | Channels | Single rate Hz | Occupancy 150 ns in % | Channels firing | Event size (bytes) | Data rate 5 KHz MB/s
BigBite | GEM | 112,640 | 2.6e9 | 17.4 | 19680 | 359,775 | 1798
 | Lead glass | 243 | _ | 100 | 243 | 1003 | 5
 | Scintillators | 360 | _ | 100 | 360 | 1485 | 7.4
 | Cerenkov | 550 | _ | 100 | 550 | 2269 | 11.34
Neutron | HCal | 288 | _ | 100 | 288 | 7,200 | 36
 | HCAL time | 288 | _ | 100 | 288 | 1170 | 5.85
 | CDET | 2152 | _ | 10 | 216 | 864 | 4.3

## Slide 9: Gen and GMn event size deconvoluted
Arm | Detector | Channels | Single rate Hz | Occupancy 100 ns in % | Channels firing | Event size (bytes) | Data rate 5 KHz MB/s
BigBite | GEM | 112,640 | 2.6e9 | 8.7 | 5248 | 62,976 | 300
 | Lead glass | 243 | _ | 100 | 243 | 1003 | 5
 | Scintillators | 360 | _ | 100 | 360 | 1485 | 7.4
 | Cerenkov | 550 | _ | 100 | 550 | 2269 | 11.34
Neutron | HCal | 288 | _ | 100 | 288 | 7,200 | 36
 | HCAL time | 288 | _ | 100 | 288 | 1170 | 5.85
 | CDET | 2152 | _ | 10 | 216 | 864 | 4.3
Total at 5 KHz 369.89 MB/s Max

## Slide 10
Bigbite
ADC
1153 channels
HCAL
288
Channels
Optical 83x100 Mbit=10 GB/s
GEM
112,640
Channels
Analog
MPD
55 Boards
1,030 MB/s in
1,800 MB/s out
(zero suppress)
SSP
3 Boards
1800 MB/s in
Deconvolution
300 MB/s out
VME
CPU
VME bus 2x100 MB/s
DAQ
Computer
369.9 MB/s
CDet
1176x2=
2352
Channels
FADC + TDC
18
Boards
42 MB/s
VME
CPU
VME bus 2x100 MB\s
1 Gbit
Ethernet x2
= 250 MB/s max
1 Gbit Ethernet x2
= 250 MB/s max
Fastbus
56 Boards in 12 crates
23.8 MB/s = 1.9 MB/s per crate
Fastbus
87 boards in 9 crates
Boards
4.3 MB/s = 1.1 MB/s crate
Swi
tch
1 Gbit Ethernet
x12
100 Mbit Ethernet
x9
1 Gbit Ethernet x2
250 MB/s max
VME
CPU
VME bus 12x20 MB\s
VME
CPU
VME bus 9x20 MB\s

## Slide 11: SILO
DAQ computer
10 GigE
IBM TS3500 9 frames ( up to 15 )
( up to 12 drives per frame)
10 LTO 5 1.5 TB 140 MB/s
6 LTO 6 2.5 TB 160 MB/s
(LTO7 6 TB 300 MB/s)
1.25 GB/s
Disk array
SSD or RAID
TS3500 frame 1000 slots : 25 K$
Data mover 10 K$ each 160 MB/s

## Slide 12: Tape cost 250 MB/s
 |  | Days | Data rate | Seconds | Total data TB | Double | DLO5 in $ | DLO6 in $ | Tape DLO6
E12-12-09-019 | GMN | 25 | 250 | 2160000 | 540 | 1080 | 54000 | 32400 | 216
E12-09-016 | GEN | 50 | 250 | 4320000 | 1080 | 2160 | 108000 | 64800 | 432
E12-07-109 | GEP/GMP | 45 | 250 | 3888000 | 972 | 1944 | 97200 | 58320 | 388.8
E12-09-018 | SIDIS | 64 | 250 | 5529600 | 1382.4 | 2764.8 | 138240 | 82944 | 552.96
 | Total | 184 |  | 15897600 | 3974.4 | 7948.8 | 397440 | 238464 | 1589.76
Actual days | Actual years |  | Time in s |  |  | Per year | 394200 | 236520 | 
368 | 1.01 | 184 | 15897600 |  |  |  |  |  | 
1 600 LTO6 tapes for 240 K$, if go to 500 MB/s 480 K$
2 frames with 8 data movers 130 K$

## Slide 13: Conclusion
Estimated rate for max 5 KHz ( expect to run at 2 to 3 KHz )
325.3 MB/s for GEp5
370 MB/s for GEn ( no geometrical correlation)
Will work on clustering and plane coincidence in SSP, reduction factor to be determined using simulation
Need implement hardware and test